Michigan’s Model School Bus Safety Inspection

________________Public Schools		Date: ____________		Bus #:____________

Model Yr:  __________________		Mileage: __________________	Hours: ____________

Inspection Cycle Compliant: yes / no (circle)

Note: School Bus Safety Inspection Cycle Maximum – 36 Day/3,500 miles/ 300 gal.

Inspector/Technician: ___________________________________________

Signature

Status Code:     √ = Item OK   N = Needs Repair     Y = Yellow Tag Item     R = Red Tag Item (place out of service)

| Status Code(s) | Inspection Items | Comments (Specific Deficiencies) |
| --- | --- | --- |
|  | BUS BODY – Interior |  |
|  | 1. Step wells/Grab Rails – decals, condition, tread wear, lighting, attachment points, metal corrosion |  |
|  | 2. Emergency Equipment – fire ext., reflective triangles (3), road flares (3), first aid kit, body fluid kit |  |
|  | 3. Documentation– registration, proof of insurance, present, readable & current |  |
|  | 4. Neutral Switch, Shifter Control – operational, indicators readable |  |
|  | 5. Dash Decals – all manufacturer decals in tact, including lift decals if applicable |  |
|  | 6. Engine Controls – key switch including alternative setting, accelerator pedal |  |
|  | 7. Gauges, Indicators, Lights, Buzzers – speed/odometer, oil, temp, fuel, volt/amp, tach, hour meter, transmission temp, filter gauge, low oil, check engine, high/low beam, turn signals, four ways, glow plugs, dash lights, pre-heater (if applicable) |  |
|  | 8. Air Brake System – gauge(s), build up, governor, parking brake, air leaks, low air warning, pop off, pedal, anti lock system lights |  |
|  | 9. Windshield Wipers $ Washers – general operation, blades, arms, reservoir, switch, pump, hose |  |
|  | 10. Heaters, Defrosters, External Dash Fan(s) – operation, condition, control speeds (all settings), plumbing/leaks, shielding, diffusers, ducts, fasteners, blades, mounting |  |
|  | 11. Dome Lights – operation, lens, switch, mounting |  |
|  | 12. Service Door – operation, control, overhead pad, glass, mounting brackets and hinge(s), seal. adjustment |  |
|  | 13. Horn – operation, control device on steering wheel |  |
|  | 14. Mirrors – adjustment, condition, discipline, convex (crossing), two rearview (each head), mirror heater system, switches |  |
|  | 15. Steering/Wheel – play, condition, operation, tilt & telescope, column, mounting secure |  |
|  | 16. Driver’s Seat/Belt – operation, condition, cover, mounting pedestal, motor, all power adjustment settings |  |
|  | 17. Passenger Seats – frames, mounting, foam, covers, bottom clips, flip up seats, modesty panels, stanchions, decals, safety belts (if applicable) |  |
|  | 18. Emergency Door(s) / Windows/ Hatches – operation, buzzers, labeling, overhead pad, stop switches and settings, hold open mechanism |  |
|  | 19. Windshield, Side & Rear Windows – cracks, fogging from laminate separation, latches, visor |  |
|  | 20. Interior Wiring, Bulkhead Seals – condition, mounting/routing, openings, electrical panel, fuses/breakers |  |
|  | 21. General Condition Bus Interior – floor, grab rail, paneling, loose objects, trip hazards, moldings, graffiti, sharp edges, screws, cleanliness and general housekeeping |  |
|  | 22. Wheelchair Lift/Access Door, Securement System (if equipped) – operation, condition, lift leaks, lighting, warning light/buzzer, door controls, outside door securement system, manual operation, chair and occupant securement system, belt cutter |  |
|  | 23. Two-Way Radio/GPS System, PA System (if applicable) – operational, mounting, wiring, condition, microphone |  |

- over –

Status Code:   √ = Item OK      N = Needs Repair     Y = Yellow Tag Item    R = Red Tag Item (place out of service)

| Status Code(s) | Inspection Items | Comments (Specific Deficiencies) |
| --- | --- | --- |
|  | BUS BODY - Exterior |  |
|  | 1. Lighting, Reflectors – headlights (high/low beam) turn signals, hazard, side marker, brake, tail, backup, clearance & ID lights, strobe, parking, license plate, all are operational, condition, lens condition, flashing, color, mounts, proper aim |  |
|  | 2. Eight Light System – operation, condition, color, lens, hood, pilot, mounts |  |
|  | 3. Stop Arms, Back Up Alarm – operation, condition, bushing/hinge, leaks, mount, decals, blade, bolts |  |
|  | 4. Batteries – condition, correct type, tie downs, terminals, cables, clean, paint condition, tray condition (properly lubricated) |  |
|  | 5. Electrical Compartment – mounting, wire routing, connections, fuses, breakers, paint condition around edges, door hinges |  |
|  | 6. General Condition, Exterior – mirror brackets, bumpers, body damage, paint (be specific in comments), grill, reflective marking, lettering, emergency door, engine hood, all brackets and hinges |  |
|  | ENGINE COMPARTMENT |  |
|  | 1. Fluid Levels – condition, brake, power steering, oil, transmission, washer, coolant, leaks |  |
|  | 2. Belts and Hoses - condition, tension, alignment, clamps |  |
|  | 3. Engine Performance – starting, shut down (stalls, hesitation, miss, skip, smoke, dieseling) |  |
|  | 4. Components – mounting, condition, brake, pump, air compressor & filter, fan/clutch, alternator, master cylinder, booster, hoses, plumbing, valves, switches, senders, gauges, l lights, turbo, leaks, air cleaner |  |
|  | 5. Wiring – routing, condition, operation, securement, type, size, connections, harness, loom |  |
|  | 6. Fuel System – condition, operation, securement connections, leaks purge fuel filter, pump, filter, lines, return springs, injectors, contamination, throttle valve |  |
|  | 7. Radiator/Cooling – mounting, cap, reservoir, fan shroud, after/inter cooler, p.s. cooler, plumbing, leaks |  |
|  | CHASSIS |  |
|  | 1. Steering – play, column, joints, steering gear, mounting, leak, pitman arm, drag link, steering arm, tie rod & ends, idler arm, alignment, condition of all grease fittings |  |
|  | 2. Frame – frame rails, cross members, chassis components, condition, securement, alignment |  |
|  | 3. Front Suspension – wheel bearings , hub, I-beam, king pins, shackles, spring mounts, springs, pins & bushings, A-frames, ball joints, U-bolts, seals, stabilizer |  |
|  | 4. Rear Suspension – axle housing, vent, differential, springs, spring mounts, U-bolts, shocks, shackles, control arms, pins, bushings, hangers, seals, wheel bearings, leaks, stabilizer, air bags (if applicable),control valve, torque suspension bolts |  |
|  | 5. Brakes – hoses, lines, chambers, slack adjusters, pushrods, linings, drums, rotors, wheel cylinders, leaks, valves, reservoirs, dryer, calibers, spring chambers, cage bolt, mounting, brackets, bleed air, hydrovac, contamination |  |
|  | 6. Mounts – engine, transmission, starter, condition, securement, alignment |  |
|  | 7. Transmission – bolts, linkage lines, filter, cooler, clutch, bearing, cylinder, modulator, leaks, programming check |  |
|  | 8. Fluid Leaks – oil, coolant, transmission, power steering, fuel |  |
|  | 9. Driveline – shafts, U-joints, yokes, hangers, guards, phasing, damper, driveshaft parking brake, mounting, condition, alignment |  |
|  | 10. Fuel Tank – leaks, mounting, hoses, wiring, cap, vent, barrier, fill nozzle |  |
|  | 11. Exhaust System – condition, leaks, mounting, muffler, tailpipe, hangers, clamps, position, extension |  |
|  | 12. Body Securement & Structure – mounts, floor, outriggers, braces, skirts, condition, securement, alignment, bolts |  |
|  | 13. Wheels & Tires – type (match), tread depth, damage, alignment, wheel hardware, pressure ck. (see comments) | Pressure : LF _____ LRI _____ LRO _____ RF _____ LRO _____ LRI _____ |